## Slide 1: SciGRID_gas workshop Berlin January 2020 Jan C. Diettrich Institute of Networked Energy Systems Adam Pluta Jan Dasenbrock Wided Medjroubi

## Slide 2: Tasks
Please start download of project from GitHub
git clone https://github.com/jdlr01/OpenSciGRID_gas.git
OR
Download from stick
Download all required libraries using on DOS/Unix prompt:
Unix pip install -r requirements.txt
Windows: pip install -r requirements_pip.txt conda install --file requirements_conda.txt

## Slide 3: Overview
Institute
SciGRID_gas project introduction
SciGRID_gas definitions
SciGRID_gas OpenStreetMap
SciGRID_gas Non-OSM data
Heuristics
Hands on data set generation

## Slide 4: Overview of the DLR-Institute of Networked Energy Systems

## Slide 5: The German Aerospace Centre (DLR)
Research institutes, aerospace-agency, project manager
Flight, aerospace, energy, transport, digitalisation and security
~8.000 employees in 40 institutes/facilities in 20 locations; Offices in Brussel, Paris, Tokyo und Washington
Turnover 2017: 922 Mio. €
Member of the Helmholtz-Gemeinschaft
Credit: Nonwarit/Fotolia

## Slide 6: Institute of Networked Energy Systems:

## Slide 7: Institute of Networked Energy Systems: Structure
City- and building- technologies
Energy system technologies
Energy system- analysis
Energy- meteorology
Energy system -modelling
Energy scenario & technology- rating
Network- technology
Flexibility and system- application
Energy- management
Sector-coupling mobility
Sector-coupling gas technic
Sector-coupling buildings

## Slide 8: Research focus
National
Regional and urban
Transnational

## Slide 9: Previous project (electricity): SciGRID (Power) GridKit
B. Wiegmans, Masterarbeit: Improving the Topology of an Electric Network Model Based (2015)
OSM: Nodes & Ways
OSM: Relations

## Slide 10: European gas transport network
(Carvalho et al. 2009) “Robustness of Trans-European Gas Networks”
  Gas covering 25% of primary energy for Europe
  Transport network ~120,000-200,000 km
  Gas-sources:
  North sea, central Asia,
  Russia, Middle east,
  Africa
  16 LNG terminals

## Slide 11: Modelling environment
Sparse data
Existing models and data only with restrictive copy/user right
Missing information on simplification and assumptions
Pipelines underground
Facility data commercially sensitive

## Slide 12
Gas network model: SciGRID_gas
For static gas- transport model
Open source
User expandable
Repeatable (GitHub)
Gas transport model data set
Python
For scientists
Open data
Data model
OSM data
Heuristic
data generation
Europe wide
Non-OSM data
CC by

## Slide 13
How to build an open gas transport data set?
Data Sources
- OSM
- GSE
- GIE
- LKD-eu
- EntsoG
- Wikipedia
- Press releases
Loading data from sources Many raw data sets
Converting into SciGRID_gas structures Many component data sets
Combining into single data set Single component data set
Generation of missing attributes Single filled component data set
Simplifying data set Single network data set 4 modelling
Single network data set

## Slide 14
www.gas.scigrid.de
Homepage & Newsletter
news.gas-subscribe@scigrid.de

## Slide 15: SciGRID_gas Definitions

## Slide 16
How to build an open gas transport data set?
Data Sources
- OSM
- GSE
- GIE
- LKD-eu
- EntsoG
- Wikipedia
- Press releases
Loading data from sources Many raw data sets
Converting into SciGRID_gas structures Many component data sets
Combining into single data set Single component data set
Generation of missing attributes Single filled component data set
Simplifying data set Single network data set 4 modelling
Single network data set
Component data set
Network data set

## Slide 17
Gas network model
Definition: Component & Attribute
LNG
LNG
storage
compressor
consumer
consumer
pipe-segment

## Slide 18
Netz.LNGs
Netz.Storages
Netz.Compressor
Netz.Consumer
Netz.PipeSegment
Component
Gas network model: Components  Attributes
LNG
LNG
storage
compressor
consumer
consumer
pipe-segment

## Slide 19
Netz.LNGs
Netz.LNGs.id
Netz.LNGs.name
Netz.LNGs.node_id
Netz.LNGs.source_id
Netz.LNGs.lat
Netz.LNGs.long
Netz.LNGs.country_code
Netz.LNGs.comment
Netz.LNGs.param
Netz.LNGs.uncertainty
Netz.LNGs.method
Component
Attribute
Gas network model: Component  Attributes
LNG
LNG
storage
compressor
consumer
consumer
pipe-segment
Dictionaries

## Slide 20
Netz.LNGs[0].name
Netz.LNGs[0].param[’max_cap_store2pipe_M_m3_per_d’]
Netz.LNGs[0].uncertainty[’max_cap_store2pipe_M_m3_per_d’]
Netz.LNGs[0].method[’max_cap_store2pipe_M_m3_per_d’]
Gas network model: Component  Attributes
LNG
LNG
storage
compressor
consumer
consumer
pipe-segment

## Slide 21
Netz.LNGs[0].param:
{ 'end_year': None, 'license': None, 'max_cap_store2pipe_M_m3_per_d': 16.71232876712329, 'max_workingGas_M_m3': 110926712.0, 'source': 'http://www.gastrade.gr/en/the-company/the-project.aspx', 'start_year': 2022.0}
Netz.LNGs[0].method:
{'end_year': None, 'license': None, 'max_cap_store2pipe_M_m3_per_d': 'raw', 'max_workingGas_M_m3': 'raw', 'source': 'raw', 'start_year': 'raw'}
Netz.LNGs[0].uncertainty:
{'end_year': -999, 'license': -999, 'max_cap_store2pipe_M_m3_per_d': 0, 'max_workingGas_M_m3': 0, 'source': 0, 'start_year': 0}
Gas network model: Component  Attributes

## Slide 22
Components
BorderPoints
Compressors
ConnectionPoints
Consumers
EntryPoints
InterConnectionPoints
LNGs
Nodes
PipeLines
PipePoints
PipeSegments
Processes
Productions
Storages
(Pressure reducer)
(Valve)
Gas network model: Components  Attributes
Nodes
Edges

## Slide 23
Gas network model : Fundamentals
Number of nodes and pipelines
complexity
Dynamic model
Static model
Entry-Exit model
Supply demand model
SciGRID_gas

## Slide 24
Gas network model : Data model
Data model e.g. LKD-EU

## Slide 25
Gas network model : Example data set: LKD-EU
Data Documentation 92: Electricity, Heat and Gas Sector Data for Modelling the German system, Friedrich Kunz, et al.

## Slide 26
Network model
Questions:
LNG
LNG
Speicher
Kompressor
Verbraucher
Verbraucher
Pipe-Segment

## Slide 27: OpenStreetMap data in

## Slide 28: Processing of OSM data in SciGRID_gas

## Slide 29: Pipelines ways in OSM

## Slide 30: Non-OSM Data

## Slide 31
Few samples
Topologically inaccurate/ accurate
Powerful:
    Gas pipeline diameter
    Gas pressure
    Storage volume
    Gas power plant
    Compressor (number of turbines/power)
Time series:
    Gas flow
    Storage
    LNG
    Production
    Consumers
Non-OSM data
POWERFUL
but
SPARSE

## Slide 32
EntsoG (Gas TSOs)
GIE (Gas Infrastructure Euro: LNG, storage) GSE (Gas Storage Euro: storage)
GB (govt)
LKD-EU (DWI)
Internet data (further data)
OPSD (Open Power System Data)
Nicht-OSM data
FNB (Fernleitungs Netz Betreib)
GasLib (Unis & OpenGridEurope)

## Slide 33
GIE
Non-OSM data
Component | #
Consumers | 0
LNGs | 21
Storages | 99
Production | 0
Compressors | 0
Pipelines | 0
Nodes | 98
https://agsi.gie.eu and https://alsi.gie.eu

## Slide 34
InternetData
Non-OSM data
Component | #
Consumers | 0
LNGs | 32
Storages | 197
Productions | 0
Compressors | 237
Pipelines [km] | 46.336
Nodes | 739
Source: various

## Slide 35
Non-OSM data
Questions:

## Slide 36: Heuristic – (Teaser)

## Slide 37
How to build an open gas transport data set?
Data Sources
- OSM
- GSE
- GIE
- LKD-eu
- EntsoG
- Wikipedia
- Press releases
Loading data from sources Many raw data sets
Converting into SciGRID_gas structures Many component data sets
Combining into single data set Single component data set
Generation of missing attributes Single filled component data set
Simplifying data set Single network data set 4 modelling
Single network data set

## Slide 38
Joining nodes through attribute names
Joining nodes through relative distance
Heuristic

## Slide 39
Attribute generation
Heuristic
Compressor
Pipe thickness
Comp. power

## Slide 40
Future:
OSM pipelines/pipe-segments joining:
  distance
  attribute
Heuristik

## Slide 41
Heuristic
OSM Non-OSM
Goal:
Joining of:
Components
Attributes

## Slide 42
Questions:
Heuristik

## Slide 43: Hands On: Pathway

## Slide 44
Hands on: Pathway
OSM
Internet
GIE
EntsoG
LKD-EU
Net rk s
NET W O RK S
Network
Individual data sets
Joining
Filling values
Simplifying network

## Slide 45
Hands on: Detailed pathway

## Slide 46
Hands on: Additional tools
Additional tools:
SciGRID_gas data input/output
SciGRID_gas data visualization

## Slide 47
Steps:
Open Anaconda prompt
Navigate to main SciGRID_gas folder
Execute “jupyter notebook”
In FF browser select “Gen_02_NonOSM.ipynb”
OR
Gen_02_NonOSM.py
Hands on: Start

## Slide 48: Hands On: Functions

## Slide 49
Hands on: Functions
Execution of Jupyter Notebook commands

## Slide 50
Hands on: Functions
2.2 Data Input/output
Netz_Internet = M_Internet.read()
NumDataSets: (Optional = 100000) number of data sets
requeYear: (Optional = '2010') string containing year [####] for which data is to be retrieved
licenseType: (Optional= ''), string containing the kind of license that the data will be selected on
GasType: (Optional = 'H') a character indicating either H or L gas.
Netz_GIE = M_GIE.read()

## Slide 51
Hands on: Functions
2.2 Data Input/output
Netz_InterNet.all()
--------------------------------------
Source InterNet
total component type count 10
--------------------------------------
BorderPoints 117
Compressors 237
ConnectionPoints 0
:
:
Processes 2
Productions 0
Storages 197
--------------------------------------
Length of PipeLines [km] 0
Length of PipeSegments [km] 46336

## Slide 52
Hands on: Functions
2.2 Data Input/output
Netz_InterNet.LNGs[0].all()
comment: country_code: GR id: Alexandroupolis lat: 40.9399278 long: 25.9940986 method: {'end_year': None, 'license': None, 'max_cap_store2pipe_M_m3_per_d': 'raw', 'max_workingGas_M_m3': 'raw', 'source': 'raw', 'start_year': 'raw'} name: Alexandroupolis node_id: ['N_521'] param: {'end_year': None, 'license': None, 'max_cap_store2pipe_M_m3_per_d': 16.71232876712329, 'max_workingGas_M_m3': 110926712.0, 'source': 'http://www.gastrade.gr/en/the-company/the-project.aspx', 'start_year': 2022.0} source_id: ['IN_Alexandroupolis'] tags: {} uncertainty: {'end_year': -999, 'license': -999, 'max_cap_store2pipe_M_m3_per_d': 0, 'max_workingGas_M_m3': 0, 'source': 0, 'start_year': 0}

## Slide 53
Hands on: Functions
2.3 CSV write
M_CSV.write('Ausgabe/InternetDaten/Data_Raw/', Netz_InterNet)

## Slide 54
Hands on: Functions
2.4 CSV read
Netz_GIE = M_CSV.read('Ausgabe/GIE/Data_Raw/')
RelDirName String containing path name of data location [default: 'Eingabe/CSV/']
NumDataSets Number of elements to be read for each component [default: 1e+100]

## Slide 55
Hands on: Functions
3 Visualization
M_Visuell.quickplot(Netz, LegendStyle = 'Str(Num)', LegendStr = '', countrycode = 'EU')
Netz An Instance of the network class
SingleColor Str , same as in Matplotlib [default: '']
SingleMarker Str , same as in Matplotlib [default: '']
Cursor Boolean, if true you can get details on mouse-click [default: False]
savefile Str, namepath [default: '']
PlotList List of plotable NetClass.Elements (e.g. Nodes, Pipelines)
IgnoreList List of ignorable NetClass.Elements (e.g. Nodes, PipeLines) [default: ['PipePoints', 'GasFlowData', 'Processes', 'Nodes', 'SourceName']
countrycode Str of 2-digit country-code - will be used for the basemap [default: 'EU']
figureNum Int, number of the figure [default: 1]
Save Boolean, to save the plot [default: False]
LegendStyle Plots name of component without number of elements ('Str') or with number of elements ('Str(Num)') [default: 'Str']

## Slide 56
How to build an open gas transport data set?
Data Sources
- OSM
- GSE
- GIE
- LKD-eu
- EntsoG
- Wikipedia
- Press releases
Loading data from sources Many raw data sets
Converting into SciGRID_gas structures Many component data sets
Combining into single data set Single component data set
Generation of missing attributes Single filled component data set
Simplifying data set Single network data set 4 modelling
Single network data set
4 Process flow overview

## Slide 57
Hands on: Functions
5.2 Loading the sources into a dictionary
DataDict = {}
DataDict['InterNet'] = Netz_InterNet
DataDict['GIE'] = Netz_GIE
# DataDict = M_LoadAdditional.loadData(
# DataLocationType = ‘Data_Raw_CSV’,
# sourceList = [‘InterNet’, ‘GIE’])

## Slide 58
How to build an open gas transport data set?
Data Sources
- OSM
- GSE
- GIE
- LKD-eu
- EntsoG
- Wikipedia
- Press releases
Loading data from sources Many raw data sets
Converting into SciGRID_gas structures Many component data sets
Combining into single data set Single component data set
Generation of missing attributes Single filled component data set
Simplifying data set Single network data set 4 modelling
Single network data set
Process flow overview

## Slide 59
Hands on: Functions
5.3 Joining the data into a single data set
Netz_Merged = JoinNetz.join(DataDict , scenaName = 'Scen_1', CompNames2Join = ['LNGs', 'Storages'])
data_sources Python dictionary of network class instances
scenaName String of scenario name selected on how to join data sets Currently the only option implemented [default: 'Scen_1']
CompNames List of component string names to join [default: []]

## Slide 60
How to build an open gas transport data set?
Data Sources
- OSM
- GSE
- GIE
- LKD-eu
- EntsoG
- Wikipedia
- Press releases
Loading data from sources Many raw data sets
Converting into SciGRID_gas structures Many component data sets
Combining into single data set Single component data set
Generation of missing attributes Single filled component data set
Simplifying data set Single network data set 4 modelling
Single network data set
4 Process flow overview

## Slide 61
Hands on: Detailed pathway

## Slide 62
Hands on: Background
Methods (Mn)
Linear (Lasso) Logistic Median Mean
Min
Max
Dependent variable (D)
Feature variable (Fn)
D = Mn(Fn)
D = Mn(F0, F1)
D = Mn(F0, F1, F2)

## Slide 63
Hands on: Background
A
B
C
D
A = Linear, B
A = Linear, C
A = Linear, D
A = Linear, B, C
A = Linear, B, D
A = Linear, C, D
A = Linear, B, C, D
A = Median, A
A = Mean, A
A = Min, A
A = Max, A
B = Linear, A
B = Linear, C
B = Linear, D
B = Linear, A, C
B = Linear, A, D
B = Linear, C, D
B = Linear, A, C, D
B = Median, B
B = Mean, B
B = Min, B
B = Max, B
C = Linear, A
C = Linear, B
C = Linear, D
C = Linear, A, B
C = Linear, A, D
C = Linear, B, D
C = Linear, A, B, D
C = Median, C
C = Mean, C
C = Min, C
C = Max, C
.., and many more, and which one to use??

## Slide 64
Hands on: QA

## Slide 65
Hands on: Detailed pathway
Setup up input files
Testing of method & feature combinations
User selects method & feature combination
Process of estimating attribute values

## Slide 66
Hands on: Functions
StatsAttribSettings.csv
6 Attribute data QA

## Slide 67
Hands on: Functions
6.2 Attribute data QA
M_Stats.gen_DataHists(Netz_Merged, StatsInputDirName = StatsInputDirName, DataStatsOutput = DataStatsOutput,)
Netz Instance of a network class
CompNames List of strings of components to apply this function to [default: []]
AttribNames List of strings of attributes to apply this function to [default: []]
StatsInputDirName String of relative path location of input setup files [default: 'Eingabe/Input_Settings']
DataStatsOutput String of relative path where to put plots [default: 'Ausgabe/Heuristic/StatsData']

## Slide 68
Hands on: QA

## Slide 69
Hands on: Functions
7.1 Setup files
..\OpenSciGRID_gas\Ausgabe\GeneratedNetz\02_NonOSM\SetupFiles\Method_Testing\
StatsMethodsSettings.csv

## Slide 70
Hands on: Functions
StatsAttribSettings.csv

## Slide 71
Hands on: Functions
7.2 Execution
M_Stats.gen_StatsParam(Netz_Merged, CompNames = CompNames2Test, SavePlots = True, MaxCombDepth = 1, StatsInputDirName = 'Ausgabe/GeneratedNetz/02_NonOSM/SetupFiles',
DataStatsOutput = 'Ausgabe/GeneratedNetz/02_NonOSM/StatsData')
Netz Instance of the network class
CompNames List of component name strings to carry out process [default : [] = will do all]
AttribNames List of attribute labels to carry out process [default : [] = will do all]
StatsInputDirName String of relative path where setup files can be found [default: 'Eingabe/Input_Settings']
DataStatsOutput String of relative path where to put output CSV files [default: 'Ausgabe/Heuristic/StatsData']
MaxCombDepth Int, of depth feature permutations [default: 2]

## Slide 72
Hands on: Functions
8 Selection of heuristics for attributes
.. /Ausgabe/GeneratedNetz/02_NonOSM/StatsData/
RetSummary_Compressors.csv
RetSummary_LNGs.csv
RetSummary_PipeSegments.csv
RetSummary_Storages.csv

## Slide 73
Hands on: Functions

## Slide 74
Hands on: Functions
9 Generation of missing attribute values
Netz_Merged = M_Stats.pop_Attribs(Netz_Merged, CompNames = [compName], SimSettings = SimSettings)
Netz Instance of network class
CompNames List of component strings to be carried out [default: []]
SimSettings List of settings [default: []]

## Slide 75
Hands on: Functions
Netz_Component.make_Attrib([], '', 'end_year', 'const', 2050)
CompName List of Strings of names of Component name [default =[]]
AttribNameSource String of attribute name of component where the data come from (source)
AttribNameDestination String of attribute name, into which new values will be written into.
MethodName String of method used to generate the new attribute value. Currently implemented options:
‘median’
'mean'
'min'
'max'
'const‘
[default: ‘median’]
MethodVal String or value to be used for the 'const' MethodName method.
ReplaceType String indicating to fill missing ('fill') or replace all ('replace') attribute values [default: 'fill']

## Slide 76
How to build an open gas transport data set?
Data Sources
- OSM
- GSE
- GIE
- LKD-eu
- EntsoG
- Wikipedia
- Press releases
Loading data from sources Many raw data sets
Converting into SciGRID_gas structures Many component data sets
Combining into single data set Single component data set
Generation of missing attributes Single filled component data set
Simplifying data set Single network data set 4 modelling
Single network data set
10 Generation of final network

## Slide 77
Hands on: Functions
10 Generation of final network
Netz_Final = M_Shape.moveComp2Pipe(Netz_Component.copy2(), 'Compressors', 'PipeSegments', maxDistance = 100.0)
Netz Instance of network class, best to be supplied as copy
compName String of component name
pipeName String, 'PipeLines' or 'PipeSegments'
maxDistance Integer of maximum moved distance for each element [default: 2]

## Slide 78
Hands on: Functions
Netz_Final.remove_unConnectedComponents()
Netz_Final.remove_unUsedNodes()

## Slide 79
Hands on: Questions
For static gas- transport model
Open source
User expandable
Repeatable (GitHub)
Gas transport model data set
Python
For scientists
Open data
Data model
OSM data
Heuristic
data generation
Europe wide
Non-OSM data
CC by